|  | HISEN ENTERPRISES CO., LTD. E-mail：alyce@mail.hisen.com.tw WEB SITE：http://www.hisen.com.tw TEL：886-2-8209-0214 FAX：886-2-8200-0692 |
| --- | --- |

◎HORIZONTAL QUENCHING MACHINE◎

Handles long and thin shafts.  The machine is automatic, driven by Servo Motor. It accommodates processes such as automatic loading of work pieces, high frequency, and Straightening.

Specifications: (1) Stroke: 50~800mm (2) Servo Motor Driven (3) Speed: 10~4000mm/min (4) Rotation: Transformer Motor Driven, rotational speed: 50~250rpm (5) Rotary Piece Diameter: 60mm x 3pcs, work piece diameter: 8~25mm x 2 pcs (6) Work piece length: 100~700mm (7) C.T. front-and-back moving distance: 0~100mm (8) C.T. can be adjusted both horizontally and vertically. (9) Straightening rods can be installed to the front and back of COIL. (10) Water tank with water-outflow hole: 1-1/2" x 2 pcs,