|  | HISEN ENTERPRISES CO., LTD. E-mail：alyce@mail.hisen.com.tw WEB SITE：http://www.hisen.com.tw TEL：886-2-8209-0214 FAX：886-2-8200-0692 |
| --- | --- |

- ROTARY QUENCHING MACHINE◎

The machine can be used for small shafts and gears, especially parts of cars and motorcycles.  The machine can be designed into 6 to 12 stations, automatically driven by Servo Motor to control movement and rotary table.

| Specifications： Driven by Servo Motor CT box vertical movement speed: 10~3000mm/min Stroke: 250~300mm 6 to 12 work stations on the rotary table. Rotational Speed: 50~250RPM The materials used for water tanks, tables, and work stations are "SUS" Example of work piece： | Features： Because the machine is Servo Motor driven, it can be precisely positioned, with precision plus and minus 0.02 mm. Features controller“AN101”. 16 different programs can be uploaded into the system and used for different work pieces. The number of work stations can be increased according to customer’s needs, so it’s possible to process several work pieces at the same time. Thus, it’s a lot faster and efficient. CT box itself can be minutely adjusted (plus and minus 50 mm), so it can correct COIL’s minute error. |
| --- | --- |