|  | HISEN ENTERPRISES CO., LTD. E-mail：alyce@mail.hisen.com.tw WEB SITE：http://www.hisen.com.tw TEL：886-2-8209-0214 FAX：886-2-8200-0692 |
| --- | --- |

- VERTICAL QUENCHING MACHINE◎

Used to process work piece such as shafts and gears.  The machine can be designed into single-shaft or double-shaft, according to customer’s needs.  The machine can be automatic, driven by servo motor, and the precision can be 0.1mm.

| Specifications: Driven by Servo Motor or hydraulic system. Quenching speed: 50~6000mm/min, Oil Pressure: around 4500mm/min。 Stroke: 600~2000mm。 Rotation: 50~250rpm(Transformer motor), around 90~250rpm(Hydraulic motor)。 Center can be designed into single-shaft or double-shaft. Diameter is 12mm or MT1。 The machine’s height is adjusted according to the stroke. Driven by Servo motor and ball screws. The precision can be 0.1mm. With C.T. fixed holder, it can be adjusted horizontally and vertically. |  |
| --- | --- |